Cross reactivity (CR a) of the immunoassay for compounds from the APEO and APEC classes.

| Analyte | LOD µg l-1 | IC50 µg l-1 nM-1 | CR, % |
| --- | --- | --- | --- |
| NPEO10 | 2.40 | 24.5 | 37.2 | 100 |
| NPEO9.5 | 3.06 | 16.5 | 26.0 | 148.2 |
| NPEO8 | 2.25 | 24.8 | 43.5 | 98.6 |
| NPEO7 | 2.89 | 26.8 | 50.9 | 109.3 |
| NPEO5 | 2.17 | 26.4 | 60.0 | 92.9 |
| OPEO8 | 1.60 | 8.5 | 15.3 | 287.3 |
| OPEO10 | 0.45 | 17.7 | 27.4 | 178.9 |
| NPEC1 | 63.5 | 962.9 | 3126 | 2.5 |
| NPEC2 | 2.78 | 24.2 | 68.8 | 101.2 |
| NP | 51.5 | 1033 | 4717 | 2.37 |
| Phenol | Not detectable | 0 |

a CR was defined as the ratio between the IC50 for NPEO10 and the IC50 for each of the other compounds tested.

ABBREVIATIONS

The limit of detection (LOD) was estimated as the concentration of the analyte that gives a change in signal equal to 3 times the standard deviation of the signal at zero dose (i.e., 1.03% for 21 replicates).

Inhibition concentration at 50% binding (IC50) is the analyte concentration which leads to 50% change in signal vs. the response in the absence of the analyte.

CONDITIONS

Injection volume: 50 µl; mixing coil volume: 1875 µl; flow rate: 0.375 + 0.375 ml min-1; carrier: 10 mM phosphate buffer pH 7.4, containing 150 mM NaCl, and 0.01 % (v/v) Tween 20 (PBST); substrate carrier: 1.57 mg l-1 2-NPG in PBST, also containing 2 mM· MgCl2; detection 405 nm.