Supporting Information

Mechanistic insight into the lanthanide (III) salt catalysed monoacylation of symmetrical diols from structural models.

Paul A. Clarke, Polly L. Arnold, Martin A. Smith, Louise S. Natrajan, Claire Wilson and Chuen Chan

General

All solvents used (toluene, THF, diethyl ether, hexane, pentane) were either degassed and purified by passage through activated alumina towers prior to use, or were freshly distilled from the appropriate drying regent under nitrogen, and thoroughly degassed prior to use. Diethyl ether from sodium/benzophenone ketyl, pentane from NaK alloy/benzophenone ketyl, toluene from sodium, hexane from potassium/benzophenone ketyl, and THF from potassium/benzophenone ketyl. NMR grade benzene-d6, toluene-d8 and spectroscopic grade methyl-THF were refluxed over potassium metal and transferred under reduced pressure.

Acylation with a saturated solution of CeCl3 experiment

A solution of the catalyst was prepared by adding freshly distilled THF (10.9 ml) to a flask containing CeCl3 (100 mg, 0.40 mmol). The solution was allowed to stir for 24h. The concentration of the solution was found to be 0.018 M.

The acylation reaction was carried out by adding the THF solution of CeCl3 (0.82 ml, 5 mol% CeCl3 w.r.t diol) to a flask containing meso-hydrobenzoin (64.0 mg, 0.30 mmol) under an atmosphere of nitrogen. Acetic anhydride (0.26 ml, 3.00 mmol) was added and the reaction was stirred for 24 h. After this time the mixture was diluted with ether (20 ml) and washed successively with saturated aqueous NaHCO3 (2 x 20 ml), brine (20 )ml, dried (MgSO4) and solvent removed. The composition of the resulting mixture was calculated by integration of the 1H NMR signals and was shown to be 95:5 meso-hydrobenzoin mono acetate to meso-hydrobenzoin bis acetate.

NMR studies

All NMR run on a Bruker AV400 NMR spectrometer at 400 MHz over 16 scans.

Acylation reaction with [Eu(tfc)3]

Methylene chloride was added to a round bottom flask containing meso-hydrobenzoin (8.6 mg, 0.04 mmol) and [Eu(tfc)3] (18 mg, 0.004 mmol). Acetic anhydride (3.6 (l, 0.4 mmol) was added to this stirring solution. The mixture was allowed to stir for 20 h before being diluted with ether (20 ml) and washed successively with saturated aqueous NaHCO3 (2 x 20 ml), brine (20 ml), dried (MgSO4) and the solvent removed. The composition of the resulting mixture was calculated by integration of the 1H NMR signals and was shown to be 10:90 meso-hydrobenzoin to meso-hydrobenzoin mono acetate.

meso-hydrobenzoin

A sample was prepared containing meso-hydrobenzoin (10 mg, 0.05 mmol) in CDCl3 (0.8 ml). 1H NMR (CDCl3, 400 MHz) ( 7.36 – 7.26 (10H, m), 4.85 (2H, s)

A second sample was prepared containing meso-hydrobenzoin (10 mg, 0.05 mmol) in CDCl3 (0.8 ml), to this was added [Eu(tfc)3] (4.2 mg, 0.005 mmol). 1H NMR (CDCl3, 400 MHz) ( 7.48 (10H, m), 5.22 (2H, s).

meso-hydrobenzoin mono acetate

A sample was prepared containing meso-hydrobenzoin mono acetate (10 mg, 0.04 mmol) in CD2Cl2 (0.8 ml). 1H NMR (CD2Cl2, 400 MHz) ( 7.31 – 7.21 (10 H, m), 5.81 (1H, d, J =6.1 Hz), 4.96 (1H, m), 1.96 (3H, s)

A second sample was prepared containing meso-hydrobenzoin mono acetate (10 mg, 0.04 mmol) in CD2Cl2 (0.8 ml), to this was added [Eu(tfc)3] (18 mg, 0.02 mmol). 1H NMR (CD2Cl2, 400 MHz) ( 7.44 – 7.33 (10H, m), 6.58 (0.5H, bs,), 6.50 (0.5H, bs), 5.42 (1H, m), 3.80 (0.5H bs), 3.60 (0.5H, bs) 2.27 (1.5H, s), 2.23 (1.5H, s).

Acylation using praseodymium complexes

A solution of meso-hydrobenzoin (214 mg, 1.00 mmol) in THF (2.70 ml) was added to a flask equipped with a stirrer bar containing PrCl3 (24.7 mg, 0.10 mmol) under an atmosphere of nitrogen. To this solution was added pivalic anhydride (1.01 ml, 5.00 mmol) and the mixture was stirred for 24 h. After this time the mixture was diluted with ether (20 ml) and washed successively with saturated aqueous NaHCO3 (2 x 20 ml), brine (20 ml0, dried (MgSO4) and the solvent removed. The composition of the resulting mixture was calculated by integration of the 1H NMR signals and was shown to be 33:66 meso-hydrobenzoin to meso-hydrobenzoin mono pivalate.

A solution of meso-hydrobenzoin (107 mg, 0.50 mmol) in THF (1.30 ml) added to a flask equipped with a stirrer bar containing Pr(thd)3.diol (3) (50.0 mg, 0.05 mmol) under an atmosphere of nitrogen. Acetic anhydride (0.22 ml, 2.50 mmol) was added to this solution and the mixture was allowed to stir for 24 h. After this time the mixture was diluted with ether (20 ml) and washed successively with saturated aqueous NaHCO3 (2 x 20 ml), brine (20 ml), dried (MgSO4) and the solvent removed. The composition of the resulting mixture was calculated by integration of the 1H NMR signals and was shown to be 48:52 meso-hydrobenzoin to meso-hydrobenzoin mono acetate.

A solution of meso-hydrobenzoin (214 mg, 1.00 mmol) in THF (2.70 ml) added to a flask equipped with a stirrer bar containing Pr(thd)3 (69 mg, 0.10 mmol) under an atmosphere of nitrogen. Acetic anhydride (0.22 ml, 2.50 mmol) was added to this solution and the mixture was allowed to stir for 24 h. After this time the mixture was diluted with ether (20 ml) and washed successively with saturated aqueous NaHCO3 (2 x 20 ml), brine (20 ml), dried (MgSO4) and the solvent removed. The composition of the resulting mixture was calculated by integration of the 1H NMR signals and was shown to be 42:58 meso-hydrobenzoin to meso-hydrobenzoin mono acetate.

Preparation of tris-2,2,6,6-tetramethyl-3,5-heptanedioate praesodymium meso-hydrobenzoin complex 3

All experimental procedures were performed under an atmosphere of dry, oxygen free argon or nitrogen, using standard Schlenk techniques (mechanical pump for vacuum 10-4mbar). Subsequent manipulations of isolated compounds were carried out in a glove box (Mbraun Unilab or Saffron) under a dry nitrogen atmosphere.

To a stirred solution of Pr(thd)3 in THF (500mg, 0.72mmol, 30ml) cooled to -60˚C was added a solution of meso-hydrobenzoin in THF (150mg, 0.72mmol, 15ml) drop wise over a period of 40 minutes. The resultant solution was allowed to warm slowly to room temperature over 15 hours, after which all volatiles were removed under reduced pressure. The resultant green solid was subsequently extracted into 10ml n-hexane, and cooled slowly to -30°C. The precipitated solids were isolated, and washed with 3 x 3ml cold (-60°C) n-hexane to yield analytically pure 3 in 24 % yield, 0.1226g. Single X-Ray quality crystals were grown by slow evaporation of a saturated diethylether solution of 3. 1H NMR (C6D6, 300 MHz) 22.33 (br, 1H,OH/CH), 5.73 (s, 10H, Ar), 3.85 (s, 54H, But), -1.16, 3H, CH (thd)), -7.45 (br, 2H,CH/OH), -23.51 (br, 1H, CH/OH); IR ((cm-1): 3374 (b, OH), 3312 (b, OH), 2853 (s), 1575 (s, CO), 1505 (s, CO), 1130 (m), 869 (m), 699 (m), 602 (w), 473 (w, CO-Pr); Anal. Calcd. for C47H71O8Pr: C, 62.25; H, 8.06. Found: C, 62.34; H, 8.17. 13C NMR only shows 4 weak peaks at 123.15, 155.92, 30.41, and 20.06 ppm

Reaction of Pr(thd)3 with rac-propanoate ester

A flame dried Schlenk was charged with Pr(thd)3 (100mg, 0.15mmol), and 15ml THF, and cooled to -60°C. To this was added a solution of rac-propionate ester in THF (39mg, 0.15mmol, 8ml) over a period of 30 minutes. Upon completion of addition, the reaction vessel was allowed to slowly attain room temperature over 12 hours. Subsequent removal of all volatiles in vacuo, extraction into 5ml diethylether, and cooling to -30°C, afforded single crystals of both starting materials in quantitative yield. 1H NMR (C6D6, 300 MHz) 23.01 (br, 1H,OH/CH), 6.99, (br, 4H, Ar), 6.88 (s, 2H, Ar), 6.59 (br, 2H, Ar), 5.49, (br, 2H, Ar), 4.05 (br, 54H, But), 2.02 (br, 1H,CH/OH), -0.13 (br, 3H, CH (thd), -5.42 (br, 3H, CH3), -11.34 (br, 2H, CH2)

Crystallographic data for 3.

Table 1.  Crystal data and structure refinement for prmhbz.

Identification code 	prmhbz

Empirical formula 	C102 H162 O18 Pr2

Formula weight 	1958.14

Temperature 	150(2) K

Wavelength 	0.71073 Å

Crystal system 	Triclinic

Space group 	P-1

Unit cell dimensions	a = 10.576(3) Å	= 79.191(7)°.

b = 12.662(4) Å	= 81.482(6)°.

c = 20.988(6) Å	 = 81.016(5)°.

Volume	2706.3(14) Å3

Z	1

Density (calculated)	1.201 Mg/m3

Absorption coefficient	0.948 mm-1

F(000)	1036

Crystal size	0.71 x 0.26 x 0.20 mm3

Theta range for data collection	1.78 to 28.68°.

Index ranges	-13<=h<=14, -16<=k<=16, 0<=l<=28

Reflections collected	12439

Independent reflections	12439 [R(int) = 0.0000]

Completeness to theta = 27.50°	97.4 %

Absorption correction	Semi-empirical from equivalents

Max. and min. transmission	0.482 and 0.361

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	12439 / 2 / 556

Goodness-of-fit on F2	1.019

Final R indices [I>2sigma(I)]	R1 = 0.0340, wR2 = 0.0800

R indices (all data)	R1 = 0.0433, wR2 = 0.0828

Largest diff. peak and hole	1.083 and -0.546 e.Å-3

Table 2.  Atomic coordinates  ( x 104) and equivalent  isotropic displacement parameters (Å2x 103)

for prmhbz.  U(eq) is defined as one third of  the trace of the orthogonalized Uij tensor.

________________________________________________________________________________

x	y	z	U(eq)

________________________________________________________________________________

Pr	2179(1)	7440(1)	2420(1)	29(1)

O(31)	3658(2)	7701(1)	1433(1)	36(1)

C(31)	4410(2)	7091(2)	1090(1)	32(1)

C(32)	4839(2)	5997(2)	1309(1)	34(1)

O(33)	3795(2)	5867(1)	2391(1)	35(1)

C(33)	4542(2)	5448(2)	1945(1)	30(1)

O(41)	603(2)	8376(2)	3162(1)	54(1)

C(41)	-157(3)	9251(2)	3164(1)	44(1)

C(42)	-228(2)	10079(2)	2628(1)	43(1)

O(43)	1355(2)	9222(1)	1912(1)	40(1)

C(43)	526(2)	10027(2)	2022(1)	39(1)

O(51)	967(2)	6054(1)	3046(1)	38(1)

C(51)	521(2)	5255(2)	2921(1)	31(1)

C(52)	411(2)	5104(2)	2290(1)	35(1)

O(53)	1075(2)	6745(1)	1721(1)	39(1)

C(53)	671(2)	5856(2)	1725(1)	32(1)

O(61)	4125(2)	8227(1)	2668(1)	30(1)

C(61)	4466(2)	8176(2)	3314(1)	26(1)

O(62)	2715(2)	7102(1)	3642(1)	34(1)

C(62)	4051(2)	7107(2)	3702(1)	27(1)

O(70)	6353(2)	8920(2)	2047(1)	44(1)

C(71)	5099(4)	10646(2)	1825(2)	73(1)

C(72)	6426(3)	10019(3)	1778(2)	59(1)

C(73)	7564(3)	8245(3)	2000(2)	56(1)

C(74)	7367(3)	7103(3)	2283(2)	67(1)

C(310)	4878(2)	7645(2)	395(1)	39(1)

C(311)	5692(4)	6872(3)	-28(1)	66(1)

C(312)	5702(5)	8485(3)	468(2)	93(2)

C(313)	3706(4)	8189(4)	73(2)	123(2)

C(330)	5156(2)	4272(2)	2154(1)	36(1)

C(331)	6117(3)	4303(2)	2637(1)	48(1)

C(332)	4087(3)	3605(2)	2505(1)	46(1)

C(410)	-1033(3)	9325(2)	3817(2)	56(1)

C(411)	-1829(5)	10421(3)	3850(2)	108(2)

C(412)	-177(4)	9018(4)	4383(2)	94(1)

C(413)	-1925(3)	8457(3)	3903(2)	70(1)

C(430)	415(3)	10964(2)	1436(2)	50(1)

C(431)	1694(3)	11404(3)	1285(2)	86(1)

C(432)	160(4)	10479(3)	854(2)	70(1)

C(433)	-684(3)	11873(2)	1556(2)	70(1)

C(510)	34(2)	4460(2)	3528(1)	37(1)

C(511)	-225(3)	3392(2)	3367(2)	61(1)

C(512)	1035(3)	4230(3)	4008(2)	66(1)

C(513)	-1230(3)	5029(2)	3837(2)	53(1)

C(530)	475(3)	5631(2)	1051(1)	43(1)

C(531)	1664(5)	4966(5)	810(2)	150(3)

C(532)	-721(5)	5049(4)	1089(2)	99(2)

C(533)	176(5)	6678(3)	600(2)	85(1)

C(610)	3894(2)	9211(2)	3583(1)	28(1)

C(611)	4461(3)	9515(2)	4062(1)	46(1)

C(612)	3991(3)	10493(2)	4292(2)	58(1)

C(613)	2949(3)	11153(2)	4042(1)	49(1)

C(614)	2380(3)	10851(2)	3572(2)	49(1)

C(615)	2850(2)	9883(2)	3336(1)	39(1)

C(620)	4370(2)	6883(2)	4397(1)	31(1)

C(621)	3510(3)	7191(2)	4919(1)	42(1)

C(622)	3900(3)	7026(3)	5534(1)	53(1)

C(623)	5139(3)	6571(3)	5639(1)	57(1)

C(624)	5988(3)	6245(3)	5126(2)	63(1)

C(625)	5603(3)	6402(2)	4510(1)	48(1)

C(730)	5888(3)	3723(2)	1592(1)	48(1)

________________________________________________________________________________

Table 3.   Selected bond lengths [Å] and angles  [°] for prmhbz.

_____________________________________________________

Pr-O(53)	2.3676(17)

Pr-O(43)	2.3966(18)

Pr-O(31)	2.4054(16)

Pr-O(51)	2.4066(17)

Pr-O(33)	2.4165(17)

Pr-O(41)	2.4333(17)

Pr-O(61)	2.5785(16)

Pr-O(62)	2.6507(18)

O(61)-C(61)	1.442(3)

O(62)-C(62)	1.438(3)

O(53)-Pr-O(43)	87.67(6)

O(53)-Pr-O(31)	80.77(6)

O(43)-Pr-O(31)	78.28(6)

O(53)-Pr-O(51)	70.21(6)

O(43)-Pr-O(51)	127.57(6)

O(31)-Pr-O(51)	138.56(6)

O(53)-Pr-O(33)	88.27(6)

O(43)-Pr-O(33)	148.43(6)

O(61)-Pr-O(62)	61.26(5)

C(61)-O(61)-Pr	124.53(12)

C(62)-O(62)-Pr	114.29(12)

_____________________________________________________

Symmetry transformations used to generate equivalent atoms:

Table 4.   Bond lengths [Å] and angles [°] for  prmhbz.

_____________________________________________________

Pr-O(53) 	2.3676(17)

Pr-O(43) 	2.3966(18)

Pr-O(31) 	2.4054(16)

Pr-O(51) 	2.4066(17)

Pr-O(33) 	2.4165(17)

Pr-O(41) 	2.4333(17)

Pr-O(61) 	2.5785(16)

Pr-O(62) 	2.6507(18)

O(31)-C(31) 	1.264(3)

C(31)-C(32) 	1.402(3)

C(31)-C(310) 	1.541(3)

C(32)-C(33) 	1.399(3)

O(33)-C(33) 	1.273(3)

C(33)-C(330) 	1.539(3)

O(41)-C(41) 	1.263(3)

C(41)-C(42) 	1.389(4)

C(41)-C(410) 	1.547(4)

C(42)-C(43) 	1.405(3)

O(43)-C(43) 	1.270(3)

C(43)-C(430) 	1.544(4)

O(51)-C(51) 	1.264(3)

C(51)-C(52) 	1.398(3)

C(51)-C(510) 	1.546(3)

C(52)-C(53) 	1.396(3)

O(53)-C(53) 	1.262(3)

C(53)-C(530) 	1.545(3)

O(61)-C(61) 	1.442(3)

C(61)-C(610) 	1.526(3)

C(61)-C(62) 	1.534(3)

O(62)-C(62) 	1.438(3)

C(62)-C(620) 	1.510(3)

O(70)-C(72) 	1.410(3)

O(70)-C(73) 	1.425(3)

C(71)-C(72) 	1.500(5)

C(73)-C(74) 	1.490(5)

C(310)-C(313) 	1.508(4)

C(310)-C(312) 	1.518(5)

C(310)-C(311) 	1.524(4)

C(330)-C(730) 	1.529(3)

C(330)-C(332) 	1.534(4)

C(330)-C(331) 	1.548(4)

C(410)-C(411) 	1.515(4)

C(410)-C(413) 	1.525(4)

C(410)-C(412) 	1.554(5)

C(430)-C(431) 	1.510(4)

C(430)-C(433) 	1.531(4)

C(430)-C(432) 	1.540(5)

C(510)-C(512) 	1.526(4)

C(510)-C(511) 	1.528(4)

C(510)-C(513) 	1.530(4)

C(530)-C(531) 	1.479(5)

C(530)-C(533) 	1.496(4)

C(530)-C(532) 	1.545(5)

C(610)-C(611) 	1.384(3)

C(610)-C(615) 	1.386(3)

C(611)-C(612) 	1.405(4)

C(612)-C(613) 	1.381(4)

C(613)-C(614) 	1.369(4)

C(614)-C(615) 	1.398(4)

C(620)-C(625) 	1.385(3)

C(620)-C(621) 	1.390(3)

C(621)-C(622) 	1.383(4)

C(622)-C(623) 	1.378(4)

C(623)-C(624) 	1.378(4)

C(624)-C(625) 	1.383(4)

O(53)-Pr-O(43)	87.67(6)

O(53)-Pr-O(31)	80.77(6)

O(43)-Pr-O(31)	78.28(6)

O(53)-Pr-O(51)	70.21(6)

O(43)-Pr-O(51)	127.57(6)

O(31)-Pr-O(51)	138.56(6)

O(53)-Pr-O(33)	88.27(6)

O(43)-Pr-O(33)	148.43(6)

O(31)-Pr-O(33)	70.17(5)

O(51)-Pr-O(33)	79.79(6)

O(53)-Pr-O(41)	108.85(7)

O(43)-Pr-O(41)	67.80(6)

O(31)-Pr-O(41)	143.93(6)

O(51)-Pr-O(41)	75.32(6)

O(33)-Pr-O(41)	142.33(6)

O(53)-Pr-O(61)	152.31(6)

O(43)-Pr-O(61)	88.91(6)

O(31)-Pr-O(61)	71.63(6)

O(51)-Pr-O(61)	131.24(6)

O(33)-Pr-O(61)	80.45(6)

O(41)-Pr-O(61)	95.16(7)

O(53)-Pr-O(62)	141.61(6)

O(43)-Pr-O(62)	120.08(6)

O(31)-Pr-O(62)	127.66(6)

O(51)-Pr-O(62)	71.71(5)

O(33)-Pr-O(62)	80.41(5)

O(41)-Pr-O(62)	65.21(7)

O(61)-Pr-O(62)	61.26(5)

C(31)-O(31)-Pr	135.79(15)

O(31)-C(31)-C(32)	124.3(2)

O(31)-C(31)-C(310)	115.0(2)

C(32)-C(31)-C(310)	120.7(2)

C(33)-C(32)-C(31)	124.6(2)

C(33)-O(33)-Pr	135.36(14)

O(33)-C(33)-C(32)	124.1(2)

O(33)-C(33)-C(330)	115.2(2)

C(32)-C(33)-C(330)	120.6(2)

C(41)-O(41)-Pr	140.12(18)

O(41)-C(41)-C(42)	123.8(2)

O(41)-C(41)-C(410)	114.2(3)

C(42)-C(41)-C(410)	122.0(2)

C(41)-C(42)-C(43)	123.5(2)

C(43)-O(43)-Pr	141.30(17)

O(43)-C(43)-C(42)	123.3(3)

O(43)-C(43)-C(430)	114.7(2)

C(42)-C(43)-C(430)	122.0(2)

C(51)-O(51)-Pr	135.33(15)

O(51)-C(51)-C(52)	123.9(2)

O(51)-C(51)-C(510)	114.9(2)

C(52)-C(51)-C(510)	121.2(2)

C(53)-C(52)-C(51)	124.4(2)

C(53)-O(53)-Pr	135.68(15)

O(53)-C(53)-C(52)	124.0(2)

O(53)-C(53)-C(530)	115.4(2)

C(52)-C(53)-C(530)	120.5(2)

C(61)-O(61)-Pr	124.53(12)

O(61)-C(61)-C(610)	110.70(18)

O(61)-C(61)-C(62)	104.74(17)

C(610)-C(61)-C(62)	117.00(17)

C(62)-O(62)-Pr	114.29(12)

O(62)-C(62)-C(620)	114.58(18)

O(62)-C(62)-C(61)	108.36(17)

C(620)-C(62)-C(61)	112.97(18)

C(72)-O(70)-C(73)	113.8(2)

O(70)-C(72)-C(71)	109.5(2)

O(70)-C(73)-C(74)	109.1(2)

C(313)-C(310)-C(312)	110.3(3)

C(313)-C(310)-C(311)	109.7(3)

C(312)-C(310)-C(311)	108.0(3)

C(313)-C(310)-C(31)	107.9(2)

C(312)-C(310)-C(31)	107.0(2)

C(311)-C(310)-C(31)	113.9(2)

C(730)-C(330)-C(332)	109.0(2)

C(730)-C(330)-C(33)	114.6(2)

C(332)-C(330)-C(33)	108.4(2)

C(730)-C(330)-C(331)	108.3(2)

C(332)-C(330)-C(331)	109.4(2)

C(33)-C(330)-C(331)	107.0(2)

C(411)-C(410)-C(413)	109.7(3)

C(411)-C(410)-C(41)	114.4(3)

C(413)-C(410)-C(41)	106.4(2)

C(411)-C(410)-C(412)	110.1(3)

C(413)-C(410)-C(412)	107.4(3)

C(41)-C(410)-C(412)	108.5(3)

C(431)-C(430)-C(433)	110.4(3)

C(431)-C(430)-C(432)	110.0(3)

C(433)-C(430)-C(432)	108.0(3)

C(431)-C(430)-C(43)	107.3(3)

C(433)-C(430)-C(43)	113.8(2)

C(432)-C(430)-C(43)	107.3(2)

C(512)-C(510)-C(511)	109.5(2)

C(512)-C(510)-C(513)	109.8(3)

C(511)-C(510)-C(513)	108.6(2)

C(512)-C(510)-C(51)	108.5(2)

C(511)-C(510)-C(51)	113.4(2)

C(513)-C(510)-C(51)	106.9(2)

C(531)-C(530)-C(533)	112.9(4)

C(531)-C(530)-C(53)	107.0(2)

C(533)-C(530)-C(53)	110.1(2)

C(531)-C(530)-C(532)	111.1(4)

C(533)-C(530)-C(532)	103.9(3)

C(53)-C(530)-C(532)	112.0(2)

C(611)-C(610)-C(615)	118.9(2)

C(611)-C(610)-C(61)	119.6(2)

C(615)-C(610)-C(61)	121.4(2)

C(610)-C(611)-C(612)	120.5(3)

C(613)-C(612)-C(611)	119.9(3)

C(614)-C(613)-C(612)	119.7(2)

C(613)-C(614)-C(615)	120.7(3)

C(610)-C(615)-C(614)	120.3(2)

C(625)-C(620)-C(621)	118.8(2)

C(625)-C(620)-C(62)	118.0(2)

C(621)-C(620)-C(62)	123.1(2)

C(622)-C(621)-C(620)	119.8(3)

C(623)-C(622)-C(621)	121.0(3)

C(622)-C(623)-C(624)	119.4(3)

C(623)-C(624)-C(625)	119.9(3)

C(624)-C(625)-C(620)	121.0(3)

_____________________________________________________________

Symmetry transformations used to generate equivalent atoms:

Table 5.   Anisotropic displacement parameters  (Å2x 103) for prmhbz.  The anisotropic

displacement factor exponent takes the form:  -22[ h2 a*2U11 + ...  + 2 h k a* b* U12 ]

______________________________________________________________________________

U11	U22 	U33	U23	U13	U12

______________________________________________________________________________

Pr	29(1) 	36(1)	22(1) 	-10(1)	2(1) 	-8(1)

O(31)	41(1) 	34(1)	27(1) 	-3(1)	7(1) 	1(1)

C(31)	32(1) 	38(1)	24(1) 	-4(1)	0(1) 	-4(1)

C(32)	36(1) 	36(1)	26(1) 	-5(1)	2(1) 	1(1)

O(33)	42(1) 	38(1)	23(1) 	-2(1)	3(1) 	-4(1)

C(33)	31(1) 	32(1)	29(1) 	-5(1)	-5(1) 	-3(1)

O(41)	65(1) 	38(1)	50(1) 	-13(1)	29(1) 	-10(1)

C(41)	38(1) 	40(2)	58(2) 	-26(1)	19(1) 	-16(1)

C(42)	33(1) 	39(2)	58(2) 	-21(1)	8(1) 	-7(1)

O(43)	40(1) 	41(1)	36(1) 	-9(1)	3(1) 	3(1)

C(43)	29(1) 	39(1)	50(2) 	-15(1)	-1(1) 	-8(1)

O(51)	48(1) 	40(1)	27(1) 	-4(1)	2(1) 	-16(1)

C(51)	24(1) 	28(1)	39(1) 	-2(1)	-3(1) 	1(1)

C(52)	35(1) 	27(1)	44(1) 	-7(1)	-8(1) 	-4(1)

O(53)	56(1) 	36(1)	28(1) 	-4(1)	-11(1) 	-14(1)

C(53)	32(1) 	31(1)	34(1) 	-9(1)	-10(1) 	-1(1)

O(61)	29(1) 	39(1)	21(1) 	-4(1)	2(1) 	-12(1)

C(61)	22(1) 	33(1)	25(1) 	-7(1)	0(1) 	-5(1)

O(62)	32(1) 	44(1)	29(1) 	-9(1)	-1(1) 	-13(1)

C(62)	25(1) 	28(1)	29(1) 	-6(1)	-1(1) 	-3(1)

O(70)	37(1) 	47(1)	45(1) 	-5(1)	8(1) 	-16(1)

C(71)	105(3) 	35(2)	67(2) 	2(2)	21(2) 	-18(2)

C(72)	69(2) 	62(2)	51(2) 	5(2)	-1(2) 	-41(2)

C(73)	34(1) 	87(2)	47(2) 	-13(2)	4(1) 	-9(2)

C(74)	47(2) 	74(2)	69(2) 	-17(2)	2(2) 	18(2)

C(310)	43(1) 	44(2)	24(1) 	0(1)	6(1) 	-2(1)

C(311)	98(3) 	60(2)	31(2) 	-8(1)	21(2) 	-9(2)

C(312)	154(4) 	85(3)	47(2) 	-12(2)	31(2) 	-72(3)

C(313)	70(2) 	206(5)	39(2) 	52(3)	9(2) 	44(3)

C(330)	38(1) 	35(1)	33(1) 	-1(1)	-7(1) 	-2(1)

C(331)	46(2) 	50(2)	47(2) 	4(1)	-18(1) 	-5(1)

C(332)	46(2) 	36(2)	53(2) 	1(1)	-3(1) 	-7(1)

C(410)	53(2) 	52(2)	61(2) 	-29(2)	29(2) 	-18(1)

C(411)	127(4) 	61(2)	114(3) 	-38(2)	77(3) 	-7(2)

C(412)	77(3) 	154(4)	58(2) 	-48(3)	28(2) 	-34(3)

C(413)	61(2) 	73(2)	78(2) 	-30(2)	34(2) 	-33(2)

C(430)	40(2) 	40(2)	64(2) 	-4(1)	1(1) 	-3(1)

C(431)	49(2) 	78(3)	117(3) 	24(2)	1(2) 	-25(2)

C(432)	84(3) 	61(2)	55(2) 	4(2)	-11(2) 	4(2)

C(433)	58(2) 	40(2)	100(3) 	2(2)	6(2) 	2(2)

C(510)	29(1) 	33(1)	42(1) 	6(1)	-3(1) 	-4(1)

C(511)	72(2) 	34(2)	68(2) 	5(1)	3(2) 	-11(2)

C(512)	52(2) 	80(2)	58(2) 	30(2)	-19(2) 	-21(2)

C(513)	47(2) 	46(2)	54(2) 	5(1)	12(1) 	-2(1)

C(530)	53(2) 	44(2)	38(1) 	-18(1)	-12(1) 	-4(1)

C(531)	107(4) 	254(7)	104(4) 	-134(4)	-50(3) 	88(4)

C(532)	146(4) 	115(4)	63(2) 	-19(2)	-33(3) 	-73(3)

C(533)	147(4) 	79(3)	41(2) 	-7(2)	-41(2) 	-23(3)

C(610)	27(1) 	27(1)	27(1) 	-4(1)	4(1) 	-6(1)

C(611)	57(2) 	39(2)	43(2) 	-14(1)	-19(1) 	6(1)

C(612)	88(2) 	45(2)	48(2) 	-22(1)	-18(2) 	-1(2)

C(613)	63(2) 	30(1)	50(2) 	-11(1)	8(1) 	1(1)

C(614)	40(2) 	32(1)	72(2) 	-8(1)	-4(1) 	3(1)

C(615)	35(1) 	33(1)	51(2) 	-9(1)	-9(1) 	-4(1)

C(620)	34(1) 	29(1)	28(1) 	0(1)	-2(1) 	-7(1)

C(621)	40(1) 	53(2)	32(1) 	-6(1)	-2(1) 	-3(1)

C(622)	61(2) 	68(2)	28(1) 	-7(1)	1(1) 	-17(2)

C(623)	62(2) 	76(2)	32(1) 	6(1)	-15(1) 	-21(2)

C(624)	46(2) 	94(3)	46(2) 	3(2)	-17(1) 	-1(2)

C(625)	39(1) 	63(2)	37(1) 	-2(1)	-6(1) 	4(1)

C(730)	54(2) 	38(2)	48(2) 	-9(1)	-2(1) 	6(1)

______________________________________________________________________________

Table 6.   Hydrogen coordinates ( x 104) and isotropic  displacement parameters (Å2x 10 3)

for prmhbz.

________________________________________________________________________________

x 	y 	z 	U(eq)

________________________________________________________________________________

H(32A)	5369	5599	1004	41

H(42A)	-819	10716	2674	51

H(52A)	142	4445	2242	42

H(61)	4707(19)	8470(20)	2403(11)	44

H(61A)	5427	8116	3282	32

H(62)	2280(20)	7551(19)	3844(13)	51

H(62A)	4554	6512	3481	33

H(71A)	5149	11409	1635	109

H(71B)	4730	10592	2285	109

H(71C)	4550	10347	1585	109

H(72A)	6809	10083	1315	71

H(72B)	6984	10320	2019	71

H(73D)	8168	8492	2241	67

H(73E)	7941	8291	1537	67

H(74A)	8196	6635	2250	100

H(74B)	6770	6863	2041	100

H(74C)	7005	7061	2743	100

H(31A)	6458	6526	181	99

H(31B)	5960	7278	-459	99

H(31C)	5183	6314	-76	99

H(31D)	6468	8119	670	140

H(31E)	5201	8984	745	140

H(31F)	5969	8892	37	140

H(31G)	3185	7638	27	184

H(31H)	3980	8588	-360	184

H(31I)	3191	8694	342	184

H(33D)	6801	4728	2412	72

H(33E)	6498	3562	2798	72

H(33F)	5661	4638	3005	72

H(33A)	3480	3583	2199	69

H(33B)	3629	3940	2873	69

H(33C)	4469	2865	2667	69

H(41G)	-2358	10611	3488	161

H(41H)	-1254	10971	3815	161

H(41I)	-2391	10391	4266	161

H(41D)	-720	9060	4801	141

H(41E)	463	9522	4319	141

H(41F)	266	8277	4385	141

H(41A)	-2488	8634	3556	106

H(41B)	-2452	8431	4330	106

H(41C)	-1407	7750	3878	106

H(43G)	1845	11716	1656	129

H(43H)	1678	11966	895	129

H(43I)	2386	10815	1206	129

H(43D)	79	11054	473	104

H(43E)	-640	10150	968	104

H(43F)	880	9924	752	104

H(43A)	-541	12196	1924	106

H(43B)	-1506	11576	1656	106

H(43C)	-708	12431	1163	106

H(51G)	-530	2925	3770	91

H(51H)	573	3026	3160	91

H(51I)	-884	3539	3067	91

H(51D)	740	3725	4395	99

H(51E)	1150	4910	4138	99

H(51F)	1858	3909	3798	99

H(51A)	-1573	4548	4225	80

H(51B)	-1857	5204	3520	80

H(51C)	-1069	5698	3963	80

H(53G)	2407	5352	791	224

H(53H)	1592	4833	372	224

H(53I)	1781	4272	1107	224

H(53D)	-808	4916	653	149

H(53E)	-1494	5505	1250	149

H(53F)	-619	4356	1389	149

H(53A)	899	7100	542	128

H(53B)	-607	7091	787	128

H(53C)	42	6527	175	128

H(61E)	5174	9060	4236	55

H(61B)	4389	10700	4618	70

H(61F)	2628	11815	4196	59

H(61D)	1659	11302	3403	59

H(61C)	2453	9686	3006	47

H(62C)	2656	7514	4852	51

H(62E)	3306	7229	5890	63

H(62D)	5405	6482	6060	68

H(62F)	6837	5913	5196	76

H(62B)	6193	6176	4158	58

H(73A)	5293	3694	1282	72

H(73B)	6259	2985	1766	72

H(73C)	6581	4140	1369	72

________________________________________________________________________________

Table 7.  Hydrogen bonds for prmhbz  [Å and °].

____________________________________________________________________________

D-H...A	d(D-H)	d(H...A)	d(D...A)	<(DHA)

____________________________________________________________________________

O(61)-H(61)...O(70)	0.823(10)	1.918(13)	2.707(2)	160(3)

O(62)-H(62)...O(41)	0.816(10)	2.43(3)	2.746(3)	104(2)

____________________________________________________________________________

Symmetry transformations used to generate equivalent atoms:

# Footnotes

A number of solutions of CeCl3 in dry freshly distilled THF were prepared. It was found that the average amount of CeCl3 that could be recovered from solution after filtration and removal of solvent always gave an effective concentration of 0.018 M in THF. In CH2Cl2 the effective concentration was found to be considerably lower, 0.0018 M.