The solution structure of supramolecular lanthanide triple helices revisited: application of crystal-field independent paramagnetic NMR techniques to mono- and dimetallic complexes

Stéphane Rigault, Claude Piguet,* and Jean-Claude G. Bünzli

Supporting informations

Table S1	Geometric ratio  and intercepts  obtained from plots of  vs  according to eq 8 for [Ln(L2)3]3+ (CD3CN, 298 K).

|  | H2-H3 | H2-C1 | H2-C2 | H2-C3 | H2-C4 |
| --- | --- | --- | --- | --- | --- |
| Rik (Ce-Tb)a | 0.93(5) | 0.33(3) | 0.39(3) | 0.91(4) | -0.7(3) |
| Rik (Er-Yb)b | 1.02(9) | 0.14(8) | 1.38(6) | 0.65(4) | 0.08(2) |
| Rik ([Eu(L2)3]3+)c | 1.018 | 0.213 | 0.499 | 0.591 | 16.321 |
| Fi -Rik.Fk (Ce-Tb)a | 0.02(4) | 0.04(6) | -1.1(1) | 1.10(4) | 0.6(2) |
| Fi -Rik.Fk (Er-Yb)b | 0.01(4) | 0.1(2) | -3.3(2) | 0.68(2) | 0.11(9) |
| Fi -Rik.Fk ([Eu(L2)3]3+)c | 0.030 | 0.046 | -1.037 | 1.063 | 0.578 |
|  | H3-C1 | H3-C2 | H3-C3 | H3-C4 | C1-C2 |
| Rik (Ce-Tb)a | 0.35(4) | 0.41(4) | 0.97(8) | -0.8(3) | 1.16(6) |
| Rik (Er-Yb)b | 0.15(6) | 1.3(2) | 0.64(1) | 0.08(1) | 7(4) |
| Rik ([Eu(L2)3]3+)c | 0.209 | 0.490 | 0.580 | 16.025 | 2.339 |
| Fi -Rik.Fk (Ce-Tb)a | 0.03(9) | -1.1(2) | 1.14(8) | 0.7(2) | -3.3(3) |
| Fi -Rik.Fk (Er-Yb)b | 0.1(1) | -3.2(5) | 0.66(7) | 0.09(6) | -17(11) |
| Fi -Rik.Fk ([Eu(L2)3]3+)c | 0.019 | -1.127 | 1.094 | 0.595 | -3.242 |
|  | C1-C3 | C1-C4 | C2-C3 | C2-C4 | C3-C4 |
| Rik (Ce-Tb)a | 2.7(3) | -2(1) | 2.3(3) | -1.8(8) | -0.8(3) |
| Rik (Er-Yb)b | 4(2) | 0.5(1) | 0.47(5) | 0.06(2) | 0.13(2) |
| Rik ([Eu(L2)3]3+)c | 2.772 | 76.527 | 1.185 | 32.717 | 27.607 |
| Fi –Rik.Fk (Ce-Tb)a | 3.1(3) | 1.7(7) | 5.6(3) | 4.4(5) | -0.5(2) |
| Fi –Rik.Fk (Er-Yb)b | 3.5(7) | 0.1(5) | 2.87(2) | 2.46(8) | -0.9(1) |
| Fi –Rik.Fk ([Eu(L2)3]3+)c | 2.994 | 1.465 | 5.363 | 4.107 | -0.530 |

a Values for the first isostructural series (Sm has been removed because of its faint paramagnetism).4 b Values for the second isostructural series. c Calculated from the crystal structure of [Eu(L2)3](CF3SO3)3 after averaging to D3 symmetry.4

Table S2	Geometric ratio  and intercepts  obtained from plots of  vs  according to eq 8 for [LnCo(L4)3]6+ (CD3CN, 298 K).

|  | H1-H2 | H1-H3 | H1-H4 | H1-H5 | H1-H6 | H1-H9 | H1-H10 | H1-H11 | H1-H12 | H1-H13 | H1-H14 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Rika | 1.83(6) | 1.22(3) | 1.00(5) | 1.10(8) | 0.244(7) | 0.076(2) | 1.07(6) | -4.6(7) | -0.22(1) | -0.33(2) | -0.48(2) |
| Rik (cryst.)b | 1.648 | 1.115 | 1.243 | 2.013 | 0.232 | 0.107 | 1.376 | 9.736 | -0.228 | -0.417 | -0.500 |
| Fi -Rik.Fk a | 0.01(1) | 0.01(1) | 0.01(1) | 0.01(2) | 0.011(7) | 0.004(7) | 0.00(2) | 0.5(1) | 0.044(7) | 0.04(1) | 0.06(1) |
| Fi -Rik.Fk (cryst.)b | -0.016 | -0.016 | -0.017 | -0.004 | -0.017 | -0.020 | -0.015 | 0.574 | 0.025 | 0.011 | 0.049 |
|  | H2-H3 | H2-H4 | H2-H5 | H2-H6 | H2-H9 | H2-H10 | H2-H11 | H2-H12 | H2-H13 | H2-H14 | H3-H4 |
| Rika | 0.665(9) | 0.55(1) | 0.60(3) | 0.133(2) | 0.0413(4) | 0.58(5) | -2.5(4) | -0.120(5) | -0.18(1) | -0.26(1) | 0.82(3) |
| Rik (cryst.)b | 0.677 | 0.755 | 1.222 | 0.141 | 0.065 | 0.835 | 5.909 | -0.138 | -0.253 | -0.303 | 1.115 |
| Fi -Rik.Fk a | 0.000(2) | 0.000(4) | 0.002(7) | 0.000(2) | -0.004(1) | -0.01(1) | 0.27(6) | 0.018(6) | 0.014(9) | 0.026(8) | 0.001(8) |
| F -Rik.Fk (cryst.)b | 0.000 | -0.001 | 0.007 | 0.000 | -0.002 | 0.000 | 0.314 | 0.022 | 0.014 | 0.035 | -0.001 |
|  | H3-H5 | H3-H6 | H3-H9 | H3-H10 | H3-H11 | H3-H12 | H3-H13 | H3-H14 | H4-H5 | H4-H6 | H4-H9 |
| Rika | 0.91(6) | 0.200(1) | 0.062 (0) | 0.88(6) | -3.725 | -0.180(5) | -0.27(1) | -0.39(2) | 1.11(3) | 0.24(1) | 0.075(3) |
| Rik (cryst.)b | 1.806 | 0.208 | 0.096 | 1.234 | 8.734 | -0.204 | -0.374 | -0.448 | 1.619 | 0.186 | 0.086 |
| Fi -Rik.Fk a | 0.00(1) | 0.000(1) | -0.006(1) | -0.01(1) | 0.4049 | 0.027(6) | 0.02(1) | 0.04(1) | 0.004(7) | 0.00(1) | -0.009(9) |
| Fi -Rik.Fk (cryst.)b | 0.010 | 0.000 | -0.003 | 0.001 | 0.475 | 0.034 | 0.022 | 0.053 | 0.014 | 0.001 | -0.003 |
|  | H4-H10 | H4-H11 | H4-H12 | H4-H13 | H4-H14 | H5-H6 | H5-H9 | H5-H10 | H5-H11 | H5-H12 | H5-H13 |
| Rika | 1.0(1) | -4(1) | -0.22(1) | -0.32(3) | -0.47(3) | 0.21(1) | 0.067(4) | 0.9(1) | -4.0(8) | -0.19(2) | -0.28(3) |
| Rik (cryst.)b | 1.106 | 7.831 | -0.183 | -0.335 | -0.402 | 0.115 | 0.053 | 0.683 | 4.837 | -0.113 | -0.207 |
| Fi -Rik.Fk a | -0.02(3) | -0.5(1) | 0.03(2) | 0.02(2) | 0.04(2) | -0.01(1) | -0.01(1) | -0.02(3) | 0.4(1) | 0.02(2) | 0.01(5) |
| Fi -Rik.Fk (cryst.)b | 0.002 | -0.142 | 0.0417 | 0.027 | 0.065 | -0.012 | -0.015 | -0.011 | 0.495 | 0.025 | 0.012 |
|  | H5-H14 | H6-H9 | H6-H10 | H6-H11 | H6-H12 | H6-H13 | H6-H14 | H9-H10 | H9-H11 | H9-H12 | H9-H13 |
| Rika | -0.42(4) | 0.311(3) | 4.4(3) | -19(3) | -0.90(2) | -1.34(6) | -1.96(9) | 14(1) | -60(10) | -2.90(9) | -4.3(2) |
| Rik (cryst.)b | -0.248 | 0.462 | 5.941 | 42.050 | -0.983 | -1.801 | -2.159 | 12.870 | 91.088 | -2.130 | -3.901 |
| Fi -Rik.Fk a | 0.03(2) | -0.03(1) | -0.07(7) | 2.0(5) | 0.13(3) | 0.11(6) | 0.20(5) | -0.1(2) | 7(1) | 0.5(1) | 0.4(2) |
| Fi -Rik.Fk (crystal)b | 0.045 | -0.015 | 0.004 | 2.371 | 0.170 | 0.110 | 0.265 | 0.062 | 7.711 | 0.597 | 0.403 |
|  | H9-H14 | H10-H11 | H10-H12 | H10-H13 | H10-H14 | H11-H12 | H11-H13 | H11-H14 | H12-H13 | H12-H14 | H13-H14 |
| Rika | -6.3(3) | -4.2(7) | -0.202(9) | -0.30(2) | -0.44(2) | 0.042(7) | 0.06(1) | 0.09(1) | 1.48(5) | 2.17(6) | 1.45(6) |
| Rik (crystal)b | -4.677 | 7.078 | -0.165 | -0.303 | -0.363 | -0.023 | -0.043 | -0.051 | 1.832 | 2.196 | 1.199 |
| Fi -Rik.Fk a | 0.7(4) | 0.48(9) | 0.04(1) | 0.04(1) | 0.06(1) | 0.106(8) | 0.11(1) | 0.103(8) | 0.03(4) | -0.07(7) | -0.06(3) |
| Fi -Rik.Fk (crystal)b | 0.902 | 0.541 | 0.037 | 0.024 | 0.059 | 0.120 | 0.123 | 0.115 | 0.067 | -0.106 | -0.115 |

a Values for the isostructural series (Ln = Ce-Yb, Sm has been removed because of its faint paramagnetism). b Calculated from the crystal structure of [LaCo(L4)3](ClO4)5.5(OH)0.5 after averaging to C3 symmetry.7

Table S3	Geometric ratio  obtained from plots of  vs  according to eq 13 for [Ln2(L5-2H)3] (D2O, 298 K).

| Rik | bCH2-H3 | bCH2-H4 | bCH2-H5 | bCH2-H4' | bCH2-H6' | bCH2-H7' | H3-H4 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (Ce-Yb)a | -0.32(1) | -0.33(1) | -0.27(1) | 0.049(2) | 2.3(4) | d | 1.03(3) |
| d = 8.81 Åb | -0.250 | -0.296 | -0.210 | 0.051 | 4.433 | -2.048 | 1.183 |
| d = 8.44 Åc | -0.200 | -0.246 | -0.183 | 0.042 | 13.175 | -1.273 | 1.234 |
| d = 8.62 Åc | -0.150 | -0.193 | -0.151 | 0.032 | -5.977 | -0.788 | 1.285 |
| d = 8.99 Åc | -0.303 | -0.344 | -0.233 | 0.059 | 3.053 | -3.500 | 1.134 |
| d = 9.18 Åc | -0.389 | -0.389 | -0.253 | 0.068 | 2.488 | -7.241 | 1.085 |
|  | H3-H5 | H3-H4' | H3-H6' | H3-H7' | H4-H5 | H4-H4' | H4-H6' |
| (Ce-Yb)a | 0.84(2) | -0.15(1) | -7(1) | d | 0.82(1) | -0.15(1) | -7(1) |
| d = 8.81 Åb | 0.839 | -0.202 | -17.713 | -2.210 | 0.709 | -0.171 | -14.968 |
| d = 8.44 Åc | 0.917 | -0.208 | -66.035 | 6.379 | 0.743 | -0.169 | -53.520 |
| d = 8.62 Åc | 1.003 | -0.215 | 39.797 | 5.247 | 0.781 | -0.167 | 30.963 |
| d = 8.99 Åc | 0.769 | -0.195 | -10.076 | 11.551 | 0.678 | -0.172 | -8.887 |
| d = 9.18 Åc | 0.705 | -0.189 | -6.945 | 20.209 | 0.650 | -0.174 | -6.401 |
|  | H4-H7' | H5-H4' | H5-H6' | H5-H7' | H4'-H6' | H4'-H7' | H6'-H7' |
| (Ce-Yb)a | d | -0.18(1) | -8.7(1.2) | d | 46(7) | d | d |
| d = 8.81 Åb | 6.915 | -0.015 | 0.004 | 0.005 | 87.771 | -40.549 | -0.462 |
| d = 8.44 Åc | 5.170 | -0.227 | -72.040 | 6.959 | 316.962 | -30.620 | -0.097 |
| d = 8.62 Åc | 4.082 | -0.214 | 39.667 | 5.230 | -185.049 | -24.398 | 0.132 |
| d = 8.99 Åc | 10.187 | -0.254 | -13.105 | 15.023 | 51.576 | -59.123 | -1.146 |
| d = 9.18 Åc | 18.625 | -0.268 | -9.848 | 28.656 | 36.760 | -106.967 | -2.910 |

a Sm has been removed because of its faint paramagnetism.9 b Calculated from the crystal structure of [Eu2(L5-2H)3] after averaging to D3 symmetry.9  c Calculated from the crystal structure of [Eu2(L5-2H)3] with a fixed intermetallic distance and after averaging to D3 symmetry (see text).  d No Rik values are obtained (see text).

Table S4	Comparison of  calculated from the crystal structure of [LaCo(L4)3](ClO4)5.5 (OH)0.5 after averaging the axial coordinates (Rik(crystA)) or the dipolar factors of each strand (Rik(crystB)) to C3 symmetry.a

|  | H1-H2 | H1-H3 | H1-H4 | H1-H5 | H1-H6 | H1-H9 |
| --- | --- | --- | --- | --- | --- | --- |
| Rik(crystA) | 1.648 | 1.115 | 1.243 | 2.013 | 0.232 | 0.107 |
| Rik(crystB) | 1.648 | 1.115 | 1.248 | 2.013 | 0.233 | 0.107 |
|  | H1-H10 | H1-H11 | H1-H12 | H1-H13 | H1-H14 |  |
| Rik(crystA) | 1.376 | 9.736 | -0.228 | -0.417 | -0.500 |  |
| Rik(crystB) | 1.379 | 14.033 | -0.228 | -0.418 | -0.506 |  |

a A complete set of Rik data can be generated according to .