Experimental parameters for the potentiometric study of PEA and its complexation to copper(II) is summarised in Table 1.

| Table 1 Summary of experimental parameters for the potentiometric study of the PEA/Cu(II) system. |  |  |
| --- | --- | --- |
| Solution composition |  |  |
| [TL] range/mol dm-3 |  | 7.5 x 10-4 - 8.0 x 10-4 |
| [TCu] range/mol dm-3 |  | 1.5 x 10-3 - 8.0 x 10-4 |
| I/mol dm-3, electrolyte |  | 0.1, KCl |
| pH Range |  | 3 - 10.5 |
| Experimental method |  | pH Titration, calibrated by standard buffers |
| T/°C |  | 25 ± 0.1 |
| Total number of data points |  |  |
| Protonation |  | 327 (8 curves) |
| Copper complexation |  | 205 (6 curves) |
| Method of Calculation |  | SUPERQUAD |

Experimental parameters for the spectrophotometeric study of PEA and its complexation to copper(II) are summarised in Table 2.

| Table 2 Summary of experimental parameters for the spectrophotometric study of the Cu(II)/PEA system |  |  |
| --- | --- | --- |
| Solution composition |  |  |
| [TL] range/mol dm-3 |  | 1.5 x 10-3 - 1.2 x 10-3 |
| [TCu] range/mol dm-3 |  | 2.7 x 10-3 -1.1 x 10-3 |
| I/mol dm-3, electrolyte |  | 0.1, KCl |
| pH Range |  | 3 - 10.5 |
| Experimental method |  | Spectrophotometric Titration (400-900nm) |
| T/°C |  | 25 ± 0.1 |
| Total number of data points |  |  |
| Copper complexation |  | 2x[spectra at 28 H+ concentrations 26 wavelengths] = 1456 points |
| Method of Calculation |  | HYPERQUAD |

Crystalographic Experimental

(by least-squares refinement on diffractometer angles for 25 automatically centred reflections, in the range 19.4 < 2 < 24.9° ,  = 0.71069 Å), Dc = 1.391 g cm-3, F(000) = 6978. Blue block crystal. Approximate crystal dimensions 0.50 x 0.40 x 0.35 mm,

Data collection and processing. Rigaku AFC7S diffractometer with graphite monochromated MoK radiation; Decay correction (8.26% decline), and absorption correction (trans. factors: 0.5476 and 0.6458) were required. Corrections were made for Lorentz and polarisation effects.