Table 1.  Crystal data and structure refinement for [Cu3(CN)3(pyr)2].

Identification code 	[Cu3(CN)3(pyr)2]

Empirical formula 	C11H8Cu3N7

Formula weight 	428.86

Temperature 	115(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	C2/m

Unit cell dimensions	a = 12.536(3) Å	= 90.

b = 10.2034(19) Å	= 93.544(4).

c = 5.5845(11) Å	 = 90.

Volume	713.0(2) Å3

Z	2

Density (calculated)	1.998 Mg/m3

Absorption coefficient	4.435 mm-1

F(000)	420

Crystal size	0.17 x 0.11 x 0.09 mm3

Theta range for data collection	2.58 to 28.27.

Index ranges	-14<=h<=16, -13<=k<=8, -7<=l<=7

Reflections collected	2370

Independent reflections	913 [R(int) = 0.0557]

Completeness to theta = 28.27	97.2 %

Absorption correction	SADABS

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	913 / 0 / 57

Goodness-of-fit on F2	1.072

Final R indices [I>2sigma(I)]	R1 = 0.0564, wR2 = 0.1406

R indices (all data)	R1 = 0.0680, wR2 = 0.1568

Extinction coefficient	0.0004(19)

Largest diff. peak and hole	2.301 and -1.322 e.Å-3

Table 2.  Atomic coordinates  ( x 104) and equivalent  isotropic displacement parameters (Å2x 103) for [Cu3(CN)3(pyr)2].  U(eq) is defined as one third of  the trace of the orthogonalized Uij tensor.

______________________________________________________________________________

x	y	z	U(eq)

______________________________________________________________________________

Cu(1)	3078(1)	0	5962(1)	22(1)

Cu(2)	0	0	0	22(1)

N(4)	2767(3)	1545(3)	8319(6)	16(1)

N(1)	4556(5)	0	5252(10)	21(1)

N(2)	1820(5)	0	3702(11)	21(1)

N(3)	1104(5)	0	2343(11)	23(1)

C(1)	4556(5)	0	5252(10)	21(1)

C(2)	1820(5)	0	3702(11)	21(1)

C(3)	1104(5)	0	2343(11)	23(1)

C(4)	1870(3)	2269(4)	8032(7)	17(1)

C(5)	3391(3)	1812(4)	10297(7)	19(1)

______________________________________________________________________________

Table 3.   Bond lengths [Å] and angles [] for  [Cu3(CN)3(pyr)2].

_____________________________________________________

Cu(1)-N(1) 	1.919(6)

Cu(1)-N(2) 	1.957(7)

Cu(1)-N(4) 	2.105(3)

Cu(1)-N(4)#1 	2.105(3)

Cu(2)-N(3) 	1.845(7)

Cu(2)-C(3)#2 	1.845(7)

Cu(2)-N(3)#2 	1.845(7)

N(4)-C(5) 	1.341(5)

N(4)-C(4) 	1.347(5)

N(1)-C(1)#3 	1.165(12)

N(1)-N(1)#3 	1.165(12)

N(2)-N(3) 	1.139(10)

C(4)-C(5)#4 	1.377(6)

C(5)-C(4)#4 	1.377(6)

N(1)-Cu(1)-N(2)	128.0(2)

N(1)-Cu(1)-N(4)	110.34(14)

N(2)-Cu(1)-N(4)	103.32(15)

N(1)-Cu(1)-N(4)#1	110.34(14)

N(2)-Cu(1)-N(4)#1	103.32(15)

N(4)-Cu(1)-N(4)#1	96.95(17)

N(3)-Cu(2)-C(3)#2	180.0(4)

N(3)-Cu(2)-N(3)#2	180.0(4)

C(3)#2-Cu(2)-N(3)#2	0.0(4)

C(5)-N(4)-C(4)	115.3(4)

C(5)-N(4)-Cu(1)	123.1(3)

C(4)-N(4)-Cu(1)	121.5(3)

C(1)#3-N(1)-N(1)#3	0.0(5)

C(1)#3-N(1)-Cu(1)	177.9(7)

N(1)#3-N(1)-Cu(1)	177.9(7)

N(3)-N(2)-Cu(1)	178.4(6)

N(2)-N(3)-Cu(2)	176.6(6)

N(4)-C(4)-C(5)#4	121.6(4)

N(4)-C(5)-C(4)#4	123.1(4)

_____________________________________________________________

Symmetry transformations used to generate equivalent atoms:

#1 x,-y,z    #2 -x,-y,-z    #3 -x+1,-y,-z+1    #4 -x+1/2,-y+1/2,-z+2

Table 4.   Anisotropic displacement parameters  (Å2x 103) for [Cu3(CN)3(pyr)2].  The anisotropic displacement factor exponent takes the form:  -2p2[ h2 a*2U11 + ...  + 2 h k a* b* U12 ]

______________________________________________________________________________

U11	U22 	U33	U23	U13	U12

______________________________________________________________________________

Cu(1)	33(1) 	17(1)	16(1) 	0	5(1) 	0

Cu(2)	20(1) 	22(1)	22(1) 	0	-2(1) 	0

N(4)	21(2) 	14(2)	14(2) 	2(1)	1(1) 	0(1)

N(1)	27(3) 	15(2)	18(2) 	0	-7(2) 	0

N(2)	18(3) 	24(3)	23(3) 	0	3(2) 	0

N(3)	27(3) 	22(3)	20(3) 	0	4(2) 	0

C(1)	27(3) 	15(2)	18(2) 	0	-7(2) 	0

C(2)	18(3) 	24(3)	23(3) 	0	3(2) 	0

C(3)	27(3) 	22(3)	20(3) 	0	4(2) 	0

C(4)	17(2) 	19(2)	14(2) 	3(1)	0(1) 	0(2)

C(5)	18(2) 	19(2)	19(2) 	5(2)	0(2) 	1(2)

______________________________________________________________________________

Table 5.   Hydrogen coordinates ( x 104) and isotropic  displacement parameters (Å2x 10 3)

for [Cu3(CN)3(pyr)2].

______________________________________________________________________________

x 	y 	z 	U(eq)

______________________________________________________________________________

H(4)	1415	2145	6672	20

H(5)	4029	1354	10551	22

______________________________________________________________________________