Table 1.  Crystal data and structure refinement for [Cu2(CN)2(2,3-dmp)].

Identification code 	[Cu2(CN)2(2,3-dmp)]

Empirical formula 	C24H24Cu6N12

Formula weight 	861.79

Temperature 	115(2) K

Wavelength 	0.71073 Å

Crystal system 	Triclinic

Space group 	P-1

Unit cell dimensions	a = 9.5676(8) Å	= 80.392(2).

b = 12.8333(11) Å	= 85.036(2).

c = 12.9090(11) Å	 = 71.907(2).

Volume	1484.5(2) Å3

Z	2

Density (calculated)	1.928 Mg/m3

Absorption coefficient	4.258 mm-1

F(000)	852

Crystal size	0.27 x 0.13 x 0.11 mm3

Theta range for data collection	1.60 to 28.30.

Index ranges	-11<=h<=12, -16<=k<=17, -16<=l<=14

Reflections collected	9756

Independent reflections	6704 [R(int) = 0.0269]

Completeness to theta = 28.30	90.8 %

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	6704 / 0 / 379

Goodness-of-fit on F2	1.051

Final R indices [I>2sigma(I)]	R1 = 0.0660, wR2 = 0.1724

R indices (all data)	R1 = 0.0889, wR2 = 0.1843

Largest diff. peak and hole	5.657 and -1.168 e.Å-3

Table 2.  Atomic coordinates  ( x 104) and equivalent  isotropic displacement parameters (Å2x 103) for [Cu2(CN)2(2,3-dmp)].  U(eq) is defined as one third of  the trace of the orthogonalized Uij tensor.

______________________________________________________________________________

x	y	z	U(eq)

______________________________________________________________________________

Cu(1)	-4217(1)	5923(1)	5027(1)	22(1)

Cu(2)	-1630(1)	2422(1)	3641(1)	19(1)

Cu(3)	3287(1)	-275(1)	3225(1)	18(1)

Cu(4)	1238(1)	106(1)	1731(1)	18(1)

Cu(5)	-1554(1)	3834(1)	-47(1)	17(1)

Cu(6)	-3820(1)	7431(1)	1268(1)	17(1)

N(13)	7012(6)	1587(5)	3217(5)	16(1)

N(14)	4996(6)	455(4)	3018(4)	16(1)

N(15)	-2451(6)	-1753(5)	1673(5)	17(1)

N(16)	-473(6)	-626(5)	1927(4)	16(1)

N(17)	-2182(6)	4373(5)	-1570(5)	19(1)

N(18)	-3481(6)	5391(5)	-3473(5)	18(1)

N(1)	-3175(7)	4629(5)	4379(5)	18(1)

N(2)	-2521(7)	3817(5)	4040(6)	24(1)

N(3)	243(7)	1322(5)	3627(5)	17(1)

N(4)	1375(8)	696(6)	3448(5)	26(2)

N(5)	4268(7)	-1740(5)	3955(5)	16(1)

N(6)	4857(7)	-2613(5)	4391(5)	21(1)

N(7)	4280(7)	-1474(5)	1304(5)	16(1)

N(8)	3155(8)	-862(5)	1507(5)	23(1)

N(9)	257(6)	1566(5)	979(5)	15(1)

N(10)	-382(8)	2431(6)	552(5)	26(2)

N(11)	-2613(7)	5166(5)	546(5)	18(1)

N(12)	-3118(7)	6022(6)	844(6)	26(2)

C(1)	-3175(7)	4629(5)	4379(5)	18(1)

C(2)	-2521(7)	3817(5)	4040(6)	24(1)

C(3)	243(7)	1322(5)	3627(5)	17(1)

C(4)	1375(8)	696(6)	3448(5)	26(2)

C(5)	4268(7)	-1740(5)	3955(5)	16(1)

C(6)	4857(7)	-2613(5)	4391(5)	21(1)

C(7)	4280(7)	-1474(5)	1304(5)	16(1)

C(8)	3155(8)	-862(5)	1507(5)	23(1)

C(9)	257(6)	1566(5)	979(5)	15(1)

C(10)	-382(8)	2431(6)	552(5)	26(2)

C(11)	-2613(7)	5166(5)	546(5)	18(1)

C(12)	-3118(7)	6022(6)	844(6)	26(2)

C(13)	6010(7)	1967(5)	2469(5)	16(1)

C(14)	4991(7)	1397(5)	2352(5)	16(1)

C(15)	6038(8)	72(5)	3743(6)	19(1)

C(16)	7023(8)	632(5)	3839(6)	20(1)

C(17)	6007(8)	3013(6)	1729(6)	23(2)

C(18)	3932(8)	1782(6)	1489(6)	23(2)

C(19)	-1449(7)	-2147(5)	2430(5)	16(1)

C(20)	-460(7)	-1562(6)	2569(6)	18(1)

C(21)	-1483(8)	-235(6)	1192(6)	20(1)

C(22)	-2477(7)	-785(5)	1066(6)	18(1)

C(23)	-1464(8)	-3208(6)	3118(6)	22(2)

C(24)	605(8)	-1972(6)	3443(6)	25(2)

C(25)	-3248(8)	4059(6)	-1912(6)	22(2)

C(26)	-3883(8)	4552(6)	-2865(6)	21(1)

C(27)	-1762(7)	5204(6)	-2167(6)	19(1)

C(28)	-575(8)	5547(7)	-1772(6)	26(2)

C(29)	-2436(7)	5721(5)	-3130(6)	18(1)

C(30)	-1994(10)	6653(7)	-3783(6)	31(2)

______________________________________________________________________________

Table 3.   Bond lengths [Å] and angles [] for  [Cu2(CN)2(2,3-dmp)].

_____________________________________________________

Cu(1)-C(6)#1 	1.888(7)

Cu(1)-N(6)#1 	1.888(7)

Cu(1)-N(1) 	1.934(6)

Cu(1)-N(18)#2 	2.052(6)

Cu(2)-N(2) 	1.866(7)

Cu(2)-N(3) 	1.907(6)

Cu(2)-N(13)#3 	2.077(6)

Cu(3)-N(4) 	1.896(7)

Cu(3)-N(5) 	1.941(6)

Cu(3)-N(14) 	2.101(6)

Cu(3)-Cu(4) 	2.7467(12)

Cu(4)-N(8) 	1.898(7)

Cu(4)-N(9) 	1.947(6)

Cu(4)-N(16) 	2.105(6)

Cu(5)-N(10) 	1.878(7)

Cu(5)-N(11) 	1.939(6)

Cu(5)-N(17) 	2.048(6)

Cu(6)-N(12) 	1.880(7)

Cu(6)-C(7)#1 	1.924(6)

Cu(6)-N(7)#1 	1.924(6)

Cu(6)-N(15)#4 	2.058(6)

N(13)-C(13) 	1.342(9)

N(13)-C(16) 	1.346(9)

N(13)-Cu(2)#5 	2.077(6)

N(14)-C(15) 	1.347(9)

N(14)-C(14) 	1.360(8)

N(15)-C(22) 	1.348(8)

N(15)-C(19) 	1.352(9)

N(15)-Cu(6)#6 	2.058(6)

N(16)-C(21) 	1.335(9)

N(16)-C(20) 	1.338(9)

N(17)-C(25) 	1.337(9)

N(17)-C(27) 	1.354(9)

N(18)-C(29) 	1.332(9)

N(18)-C(26) 	1.359(9)

N(18)-Cu(1)#7 	2.052(6)

N(1)-N(2) 	1.171(9)

N(3)-N(4) 	1.162(9)

N(5)-N(6) 	1.158(9)

N(6)-Cu(1)#8 	1.888(7)

N(7)-N(8) 	1.157(9)

N(7)-Cu(6)#8 	1.924(6)

N(9)-N(10) 	1.159(9)

N(11)-N(12) 	1.169(9)

C(13)-C(14) 	1.419(9)

C(13)-C(17) 	1.513(9)

C(14)-C(18) 	1.488(10)

C(15)-C(16) 	1.376(10)

C(19)-C(20) 	1.417(10)

C(19)-C(23) 	1.500(9)

C(20)-C(24) 	1.503(10)

C(21)-C(22) 	1.382(10)

C(25)-C(26) 	1.384(10)

C(27)-C(29) 	1.414(10)

C(27)-C(28) 	1.493(10)

C(29)-C(30) 	1.495(10)

C(6)#1-Cu(1)-N(6)#1	0.0(6)

C(6)#1-Cu(1)-N(1)	129.4(3)

N(6)#1-Cu(1)-N(1)	129.4(3)

C(6)#1-Cu(1)-N(18)#2	128.2(3)

N(6)#1-Cu(1)-N(18)#2	128.2(3)

N(1)-Cu(1)-N(18)#2	99.9(2)

N(2)-Cu(2)-N(3)	140.3(3)

N(2)-Cu(2)-N(13)#3	117.7(3)

N(3)-Cu(2)-N(13)#3	101.4(2)

N(4)-Cu(3)-N(5)	130.3(3)

N(4)-Cu(3)-N(14)	115.7(3)

N(5)-Cu(3)-N(14)	101.6(2)

N(4)-Cu(3)-Cu(4)	61.5(2)

N(5)-Cu(3)-Cu(4)	123.21(18)

N(14)-Cu(3)-Cu(4)	122.54(16)

N(8)-Cu(4)-N(9)	129.7(3)

N(8)-Cu(4)-N(16)	115.8(3)

N(9)-Cu(4)-N(16)	101.2(2)

N(8)-Cu(4)-Cu(3)	61.5(2)

N(9)-Cu(4)-Cu(3)	123.91(18)

N(16)-Cu(4)-Cu(3)	122.91(15)

N(10)-Cu(5)-N(11)	132.5(3)

N(10)-Cu(5)-N(17)	128.9(3)

N(11)-Cu(5)-N(17)	98.6(2)

N(12)-Cu(6)-C(7)#1	134.3(3)

N(12)-Cu(6)-N(7)#1	134.3(3)

C(7)#1-Cu(6)-N(7)#1	0.0(3)

N(12)-Cu(6)-N(15)#4	122.9(3)

C(7)#1-Cu(6)-N(15)#4	102.4(2)

N(7)#1-Cu(6)-N(15)#4	102.4(2)

C(13)-N(13)-C(16)	117.0(6)

C(13)-N(13)-Cu(2)#5	126.4(4)

C(16)-N(13)-Cu(2)#5	116.1(5)

C(15)-N(14)-C(14)	117.4(6)

C(15)-N(14)-Cu(3)	115.9(5)

C(14)-N(14)-Cu(3)	125.4(5)

C(22)-N(15)-C(19)	117.5(6)

C(22)-N(15)-Cu(6)#6	116.5(5)

C(19)-N(15)-Cu(6)#6	125.7(5)

C(21)-N(16)-C(20)	118.3(6)

C(21)-N(16)-Cu(4)	114.9(5)

C(20)-N(16)-Cu(4)	125.3(5)

C(25)-N(17)-C(27)	118.4(6)

C(25)-N(17)-Cu(5)	119.2(5)

C(27)-N(17)-Cu(5)	121.1(5)

C(29)-N(18)-C(26)	118.0(6)

C(29)-N(18)-Cu(1)#7	121.6(5)

C(26)-N(18)-Cu(1)#7	119.5(5)

N(2)-N(1)-Cu(1)	176.4(6)

N(1)-N(2)-Cu(2)	171.9(6)

N(4)-N(3)-Cu(2)	169.2(6)

N(3)-N(4)-Cu(3)	175.6(7)

N(6)-N(5)-Cu(3)	179.8(7)

N(5)-N(6)-Cu(1)#8	176.1(6)

N(8)-N(7)-Cu(6)#8	168.4(6)

N(7)-N(8)-Cu(4)	174.6(6)

N(10)-N(9)-Cu(4)	177.1(6)

N(9)-N(10)-Cu(5)	174.9(7)

N(12)-N(11)-Cu(5)	171.7(6)

N(11)-N(12)-Cu(6)	175.8(6)

N(13)-C(13)-C(14)	121.5(6)

N(13)-C(13)-C(17)	118.4(6)

C(14)-C(13)-C(17)	120.1(6)

N(14)-C(14)-C(13)	120.1(6)

N(14)-C(14)-C(18)	118.3(6)

C(13)-C(14)-C(18)	121.6(6)

N(14)-C(15)-C(16)	121.5(6)

N(13)-C(16)-C(15)	122.4(6)

N(15)-C(19)-C(20)	120.8(6)

N(15)-C(19)-C(23)	116.8(6)

C(20)-C(19)-C(23)	122.4(6)

N(16)-C(20)-C(19)	120.3(6)

N(16)-C(20)-C(24)	119.0(6)

C(19)-C(20)-C(24)	120.7(6)

N(16)-C(21)-C(22)	121.8(6)

N(15)-C(22)-C(21)	121.2(6)

N(17)-C(25)-C(26)	120.9(7)

N(18)-C(26)-C(25)	121.5(6)

N(17)-C(27)-C(29)	120.4(6)

N(17)-C(27)-C(28)	117.7(6)

C(29)-C(27)-C(28)	121.9(6)

N(18)-C(29)-C(27)	120.8(6)

N(18)-C(29)-C(30)	118.6(6)

C(27)-C(29)-C(30)	120.6(6)

_____________________________________________________________

Symmetry transformations used to generate equivalent atoms:

#1 x-1,y+1,z    #2 x,y,z+1    #3 x-1,y,z    #4 x,y+1,z

#5 x+1,y,z    #6 x,y-1,z    #7 x,y,z-1    #8 x+1,y-1,z

Table 4.   Anisotropic displacement parameters  (Å2x 103) for [Cu2(CN)2(2,3-dmp)].  The anisotropic displacement factor exponent takes the form:  -2p2[ h2 a*2U11 + ...  + 2 h k a* b* U12 ]

______________________________________________________________________________

U11	U22 	U33	U23	U13	U12

______________________________________________________________________________

Cu(1)	26(1) 	16(1)	19(1) 	0(1)	-8(1) 	1(1)

Cu(2)	18(1) 	12(1)	24(1) 	-3(1)	-1(1) 	-1(1)

Cu(3)	17(1) 	10(1)	24(1) 	1(1)	-2(1) 	-1(1)

Cu(4)	14(1) 	12(1)	23(1) 	1(1)	-4(1) 	1(1)

Cu(5)	16(1) 	14(1)	21(1) 	1(1)	-7(1) 	-3(1)

Cu(6)	16(1) 	11(1)	21(1) 	-2(1)	-2(1) 	0(1)

N(13)	15(3) 	13(3)	20(3) 	-4(2)	-5(2) 	-2(2)

N(14)	19(3) 	11(3)	14(3) 	0(2)	-2(2) 	2(2)

N(15)	12(3) 	16(3)	18(3) 	-1(2)	2(2) 	1(2)

N(16)	14(3) 	15(3)	15(3) 	-1(2)	-3(2) 	-1(2)

N(17)	20(3) 	14(3)	21(3) 	-2(2)	-3(2) 	-2(2)

N(18)	23(3) 	12(3)	20(3) 	-3(2)	-4(2) 	-5(2)

N(1)	19(3) 	14(3)	19(3) 	-1(2)	-7(2) 	-1(2)

N(2)	22(3) 	20(3)	30(4) 	-1(3)	-7(3) 	-9(3)

N(3)	14(3) 	15(3)	23(3) 	-6(2)	-5(2) 	-2(2)

N(4)	33(4) 	21(3)	22(4) 	-1(3)	-2(3) 	-8(3)

N(5)	19(3) 	11(3)	17(3) 	1(2)	-3(2) 	-4(2)

N(6)	19(3) 	22(3)	23(3) 	-7(3)	-1(3) 	-7(3)

N(7)	16(3) 	10(3)	18(3) 	-2(2)	-6(2) 	4(2)

N(8)	27(4) 	16(3)	23(4) 	2(3)	-5(3) 	-5(3)

N(9)	15(3) 	9(3)	19(3) 	1(2)	-5(2) 	1(2)

N(10)	27(4) 	26(4)	22(4) 	-5(3)	-3(3) 	-3(3)

N(11)	18(3) 	12(3)	21(3) 	-3(2)	-3(2) 	0(2)

N(12)	21(3) 	25(4)	28(4) 	3(3)	-5(3) 	-6(3)

C(1)	19(3) 	14(3)	19(3) 	-1(2)	-7(2) 	-1(2)

C(2)	22(3) 	20(3)	30(4) 	-1(3)	-7(3) 	-9(3)

C(3)	14(3) 	15(3)	23(3) 	-6(2)	-5(2) 	-2(2)

C(4)	33(4) 	21(3)	22(4) 	-1(3)	-2(3) 	-8(3)

C(5)	19(3) 	11(3)	17(3) 	1(2)	-3(2) 	-4(2)

C(6)	19(3) 	22(3)	23(3) 	-7(3)	-1(3) 	-7(3)

C(7)	16(3) 	10(3)	18(3) 	-2(2)	-6(2) 	4(2)

C(8)	27(4) 	16(3)	23(4) 	2(3)	-5(3) 	-5(3)

C(9)	15(3) 	9(3)	19(3) 	1(2)	-5(2) 	1(2)

C(10)	27(4) 	26(4)	22(4) 	-5(3)	-3(3) 	-3(3)

C(11)	18(3) 	12(3)	21(3) 	-3(2)	-3(2) 	0(2)

C(12)	21(3) 	25(4)	28(4) 	3(3)	-5(3) 	-6(3)

C(13)	18(3) 	10(3)	17(3) 	0(2)	1(2) 	-4(2)

C(14)	19(3) 	11(3)	14(3) 	0(2)	3(2) 	-3(2)

C(15)	20(3) 	12(3)	20(4) 	0(3)	0(3) 	3(3)

C(16)	21(3) 	12(3)	21(4) 	2(3)	-5(3) 	0(3)

C(17)	26(4) 	14(3)	23(4) 	5(3)	4(3) 	-4(3)

C(18)	24(4) 	20(3)	24(4) 	3(3)	-6(3) 	-6(3)

C(19)	19(3) 	10(3)	11(3) 	2(2)	3(2) 	2(2)

C(20)	16(3) 	18(3)	18(3) 	-2(3)	-2(3) 	-2(3)

C(21)	18(3) 	18(3)	22(4) 	-2(3)	-3(3) 	-4(3)

C(22)	16(3) 	12(3)	22(4) 	0(3)	-4(3) 	-1(2)

C(23)	19(3) 	23(4)	23(4) 	3(3)	-3(3) 	-7(3)

C(24)	27(4) 	20(3)	26(4) 	5(3)	-12(3) 	-5(3)

C(25)	26(4) 	14(3)	26(4) 	0(3)	-9(3) 	-8(3)

C(26)	21(3) 	17(3)	24(4) 	0(3)	-7(3) 	-6(3)

C(27)	18(3) 	17(3)	24(4) 	-8(3)	-4(3) 	-4(3)

C(28)	18(3) 	29(4)	32(4) 	0(3)	-5(3) 	-11(3)

C(29)	15(3) 	15(3)	23(4) 	0(3)	1(3) 	-4(3)

C(30)	43(5) 	35(4)	21(4) 	2(3)	-5(3) 	-22(4)

______________________________________________________________________________

Table 5.   Hydrogen coordinates ( x 104) and isotropic  displacement parameters (Å2x 10 3)

for [Cu2(CN)2(2,3-dmp)].

______________________________________________________________________________

x 	y 	z 	U(eq)

______________________________________________________________________________

H(15)	6093	-588	4189	23

H(16)	7722	341	4353	23

H(17A)	6759	3292	1916	35

H(17B)	5065	3561	1779	35

H(17C)	6195	2852	1021	35

H(18A)	3338	1294	1538	35

H(18B)	4464	1781	823	35

H(18C)	3312	2519	1547	35

H(21)	-1519	425	753	24

H(22)	-3176	-481	554	21

H(23A)	-2210	-3471	2896	33

H(23B)	-1672	-3079	3834	33

H(23C)	-521	-3753	3063	33

H(24A)	1185	-1477	3420	37

H(24B)	1240	-2700	3362	37

H(24C)	72	-2002	4107	37

H(25)	-3567	3502	-1503	26

H(26)	-4600	4303	-3096	25

H(28A)	-260	5101	-1111	39

H(28B)	-945	6313	-1680	39

H(28C)	243	5447	-2271	39

H(30A)	-2560	6904	-4405	46

H(30B)	-967	6401	-3979	46

H(30C)	-2172	7253	-3385	46

______________________________________________________________________________