Table S1:   Analytical figures of merit of HPLC-ICP-SFMS operated under low resolution (m/∆m = 300) using a conventional concentric nebulizer

|  | LOD (pg mL-1) | LOD (pg) | Repeatability (%) | Range (ng ml-1) | R2 |
| --- | --- | --- | --- | --- | --- |
| Analyte | Aa | Hb | A | H | A | H |  | A | H |
| As(III) | 3.9 | 4.8 | 0.39 | 0.48 | 0.5 | 2.1 | 0.1-20 | 0.99989 | 0.99994 |
| DMA | 4.4 | 8.2 | 0.44 | 0.82 | 1.0 | 1.6 | 0.1-20 | 0.99998 | 0.99991 |
| MMA | 5.8 | 4.0 | 0.58 | 0.40 | 1.0 | 2.4 | 0.1-20 | 0.99999 | 0.99995 |
| As(V) | 4.0 | 8.6 | 0.40 | 0.86 | 1.2 | 2.4 | 0.1-20 | 0.99999 | 1.00000 |
| AB | 2.5 | 1.9 | 0.25 | 0.19 | 2.0 | 2.1 | 0.1-20 | 0.99972 | 0.99998 |
| TMAO | 3.2 | 4.5 | 0.32 | 0.45 | 2.3 | 1.6 | 0.1-20 | 0.99926 | 0.99990 |
| AC | 2.7 | 3.3 | 0.27 | 0.33 | 1.1 | 2.8 | 0.1-20 | 0.99940 | 0.99985 |
| Tetra | 2.8 | 2.9 | 0.28 | 0.28 | 1.8 | 2.9 | 0.1-20 | 0.99957 | 0.99992 |

apeak area; bpeak height.

Detection limits were determined by making 6 repetitive injections (100 µl) of standards in the lower linear concentration range (0.1 ng/mL each) and were calculated from the standard deviations of the peak areas and peak heights (3(), respectively. Repeatability was determined from peak areas and peak heights by calculating the relative standard deviation (RSD) of four successive analysis of a standard solution containing 0.5 ng/mL each analyte.

Table S2:  	Analytical figures of merit of HPLC-ICP-SFMS operated under high resolution (m/∆m = 10,000) using a conventional concentric nebulizer

|  | LOD (pg mL-1) | LOD (pg) | Repeatability (%) | Range (ng ml-1) | R2 |
| --- | --- | --- | --- | --- | --- |
| Analyte | Aa | Hb | A | H | A | H |  | A | H |
| As(III) | 130 | 280 | 13 | 28 | 8.5 | 17.4 | 0.5-20 | 0.99974 | 0.99997 |
| DMA | 190 | 290 | 19 | 29 | 12.9 | 17.4 | 0.5-20 | 0.99995 | 0.99904 |
| MMA | 220 | 240 | 22 | 24 | 15.8 | 14.2 | 0.5-20 | 0.99998 | 0.99979 |
| As(V) | 150 | 260 | 15 | 26 | 10.4 | 15.1 | 0.5-20 | 0.99890 | 0.99894 |
| AB | 200 | 180 | 20 | 18 | 14.1 | 12.3 | 0.5-20 | 0.99840 | 0.99640 |
| TMAO | 190 | 210 | 19 | 21 | 12.9 | 15.5 | 0.5-20 | 0.99939 | 0.99784 |
| AC | 170 | 130 | 17 | 13 | 11.6 | 9.5 | 0.5-20 | 0.99975 | 0.99966 |
| Tetra | 110 | 150 | 11 | 15 | 7.1 | 11.0 | 0.5-20 | 0.99990 | 0.99976 |

*Detection limits were determined by making 6 repetitive injections (100 µl) of standards in the lower linear concentration range (0.5 ng/mL each) and were calculated from the standard deviations of the peak areas and peak heights (3(), respectively. Repeatability was determined from peak areas and peak heights by calculating the relative standard deviation (RSD) of four successive analysis of a standard solution containing 0.5 ng/mL each analyte. apeak area; bpeak height.

Table S3: Comparison of chromatographic peak resolution (R) between using concentric nebulizer and Aridus system.

|  | RDMA-AB | RAB-TMAO | RTMAO-AC | RAC-Tetra |
| --- | --- | --- | --- | --- |
| Concentric nebulizer | 0.98 | 1.49 | 1.63 | 1.33 |
| Aridus | 0.63 | 0.86 | 0.94 | 0.65 |

Table S4:	Comparison of LODs (ng/mL as As) obtained with different techniques for As speciation analysis reported in recent literatures

| Technique | As(III) | DMA | MMA | As(V) | AB | TMAO | AC | Tetra | Ref. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| HPLC-HG-AFS | 0.5 | 0.7 | 0.4 | 0.8 | --- | --- | --- | --- | Le and Ma 7 |
| HPLC-MIP-MS | --- | 1.85 | 1.67 | 2.25 | 3.07 | 13.3 | 2.63 | 2.77 | Chatterjee et al.8 |
| HPLC-USN-MIP-MS | --- | 0.73 | 0.36 | 0.46 | 0.21 | 3.64 | 0.39 | 0.32 | Chatterjee et al.8 |
| HPLC-Q-ICPMS | 0.089 0.067 0.37 0.19 0.02 | 0.25 0.074 0.32 0.16 0.08 | 0.20 0.035 --- 0.29 0.08 | 0.34 0.089 0.42 0.52 0.08 | 0.067 --- 0.33 0.16 1.0 | 0.14 --- --- 0.60 0.08 | 0.19 --- 0.38 0.58 0.08 | 0.28 --- --- 0.38 0.08 | Nakazato et al.9 Day et al.10 Mattusch et al.11 Londesborough et al.12 Kohlmeyer et al13 |
| HPLC-HHPN-Q-ICPMS | 0.20 | 0.12 | 0.06 | 0.60 | 0.09 | --- | 0.04 | --- | Zheng et al.14 |
| HPLC-HG-Q-ICPMS | 0.022 | 0.028 | 0.016 | 0.048 | --- | 0.075 | --- | --- | Nakazato et al.9 |
| HPLC-HEX-ICPMS | 0.06 | 0.1 | 0.4 | 0.05 | 0.02 | --- | --- | --- | Xie et al.15 |
| HPLC-SF-ICPMS (m/∆m = 300) | 0.090 | 0.054 | 0.076 | 0.072 | 0.049 | --- | --- | --- | Koellensperger et al.5 |
| HPLC-SF-ICPMS LR HR LR (MicroMist) | 0.0039 0.13 0.0015 | 0.0044 0.19 0.0021 | 0.0058 0.22 0.0024 | 0.0040 0.15 0.0022 | 0.0025 0.20 0.0012 | 0.0032 0.19 0.0013 | 0.0027 0.17 0.0016 | 0.0028 0.11 0.0016 | This work |

Figure captions

Figure S1. Chromatogram of separated cationic As compounds (0.2 ng/mL) with HPLC-ICP-SFMS at low resolution mode (m/( = 300) using the Aridus system as an interface.

Figure S2.  Chromatograms of As standard solutions (0.05 ng/mL) obtained with HPLC-ICP-MS at low resolution mode (m/( = 300) using the MicroMist nebulizer. A: anion-exchange chromatography; B: cation-exchange chromatography.

Figure S3. The distribution of As compounds in different tissues of Northern Pike, Esox lucius (Linnaeus).

Figure S1

Figure 2

Figure S3

# Text boxes

As(III)

As(V)

MMA

DMA