1Ba3Cu3Sc3InO12                                                     PUBTABLE Version MS-DOS 2000-10-10T23:16:29  Page   1


                   |-----------------------------------------|
                   |     Program PUBTABLES Version MS-DOS    |
                   |  Generate crystal structure data tables |
                   | Distributed on 15/ 7/1999; 0:32:10      |
                   |-----------------------------------------|

        |---------------------------------------------------------------|
        |            Allen C. Larson and Robert B. Von Dreele           |
        |      Manuel Lujan, Jr. Neutron Scattering Center, MS-H805     |
        |      Los Alamos National Laboratory, Los Alamos, NM  87545    |
        |                                                               |
        | Copyright, 1999, The Regents of the University of California. |
        |---------------------------------------------------------------|
 
 GENLES was run on 2000-10-10T23:15:53     Total cycles run 414

 The Current Least-Squares controls are

 Maximum number of cycles is   10
 I/SigI cut-off is  1.00


 Anisotropic thermal factors are defined by
   T = exp(h**2*astr**2*u11+... +2*h*k*astr*bstr*u12+... )


 Space group I 4/mcm             
 The lattice is centric  I-centered tetragonal    Laue symmetry 4/mmm 
  Multiplicity of a general site is  32
  The symmetry of the point 0,0,0 contains 1bar

 The equivalent positions are:

 ( 1)     X      Y      Z  ( 2)    -Y      X      Z 
 ( 3)    -X     -Y      Z  ( 4)     Y     -X      Z 
 ( 5)    -X      Y  1/2+Z  ( 6)    -Y     -X  1/2+Z 
 ( 7)     X     -Y  1/2+Z  ( 8)     Y      X  1/2+Z 
 

 Lattice constants are 
  a =  11.95297(30)  b = A  c =  8.42106(25) 
  Alpha =  90     Beta =  90    Gamma =  90   
 Cell volume = 1203.15(6)

  Name         X             Y             Z         Ui/Ue*100    Site sym Mult Type Seq Fractn
  BA1       .000000       .000000       .000000        .61(6)     4/M(001)   4   BA    1 1.0000      
  BA2       .27777(9)     .77777(9)     .000000        .51(5)     MM2(110)   8   BA    2 1.0000      
  CU3       .500000       .000000       .250000        .94(20)    -42M 001   4   CU    3 1.0000      
  CU4       .10603(20)    .60603(20)    .000000        .61(14)    MM2(110)   8   CU    4 1.0000      
  IN5       .24178(17)    .000000       .250000        .08          2(100)  16   IN    5  .260(3)    
  SC6       .24178(17)    .000000       .250000        .08          2(100)  16   SC    6  .740(3)    
  O7        .1169(8)      .6169(8)      .2298(11)      .03(12)      M(+-0)  16   O     7 1.0000      
  O8        .1297(8)      .1297(8)      .250000        .03(12)      2(110)  16   O     8 1.0000      
  O9        .2422(15)     .5005(6)      .000000        .03(12)      M(001)  16   O     9 1.0000      
1Ba3Cu3Sc3InO12                                                     PUBTABLE Version MS-DOS 2000-10-10T23:16:29  Page   2


 Thermal parameters multiplied by 100.0 are
  Name        U11          U22          U33          U12          U13          U23
  BA1        .61(6)       .61          .61          .00          .00          .00        
  BA2        .51(5)       .51          .51          .00          .00          .00        
  CU3        .94(20)      .94          .94          .00          .00          .00        
  CU4        .61(14)      .61          .61          .00          .00          .00        
  IN5        .08          .08          .08          .00          .00          .00        
  SC6        .08          .08          .08          .00          .00          .00        
  O7         .03(12)      .03          .03          .00          .00          .00        
  O8         .03(12)      .03          .03          .00          .00          .00        
  O9         .03(12)      .03          .03          .00          .00          .00        
Supplementary Material (ESI) for Journal of Materials Chemistry
This journal is (c) The Royal Society of Chemistry 2001